## Slide 1
STI – robot competition
Claudio Fritsche (GM)
Roman Oechslin (MT)
Héloïse Boross (MT)
20th March 2017
TEAM 3
Milestone number 3

## Slide 2: Concept
2
Introduction HW mechanics HW electronics Budget Software Management

## Slide 3: Pre-design
3
Introduction HW mechanics HW electronics Budget Software Management
WEAKNESSES
No facylities to built wood pieces
Too many screw to remove to open the robot
Too many mechanical pieces
Round shape doesn’t maximize the surface’s contact between the conveyer belt and the bottle
The thin belt which drives the sticky one will slip on the rollers

## Slide 4: Outside of the robot
4
Introduction HW mechanics HW electronics Budget Software Management
360° camera
Camera
4 x IR sensors
Bottle releaser
Aeration and access hole
Sticky conveyer belt
FRONT
BACK
2x Bumpers
Notes: Dimensions générale et explications générales

## Slide 5: Inside of the robot
5
Introduction HW mechanics HW electronics Budget Software Management
3x Batteries
5x Motors
Electonics
Roller

## Slide 6: Dimensions
6
Introduction HW mechanics HW electronics Budget Software Management
250 mm
97 mm
38 mm
31 mm
110 mm
362 mm
375 mm
419 mm
300 mm

## Slide 7: Expected capability
7
Introduction HW mechanics HW electronics Budget Software Management
from 2 to 7 bottles

## Slide 8: Sticky material
8
Introduction HW mechanics HW electronics Budget Software Management
2-Faces tape
How to fix it? (explain)
Two sided duct tape
Robust to vibration
Good repeatability
Robust to dust
Cheap solution

## Slide 9: Sticky material testing
9
Introduction HW mechanics HW electronics Budget Software Management

## Slide 10: Sticky belt fabrication
10
Introduction HW mechanics HW electronics Budget Software Management
Sewing
Taping

## Slide 11: Roller
11
Introduction HW mechanics HW electronics Budget Software Management
Sides of the robot
Round-head nut
Axle
Ball bearing
FREE AXLE
ACTUATED AXLE

## Slide 12: Sprocket testing
12
Introduction HW mechanics HW electronics Budget Software Management
Focus sur les parties à expliquer plus en détail
Sprockets test
Navigation explanation
How is the conveyor belt driven?
Bycicle chain fixed to belt
Sprockets
DC – motor

## Slide 13: Conveyoring
13
Introduction HW mechanics HW electronics Budget Software Management
1 Motor
Smooth belt
Chain

## Slide 14: Assembly
14
Introduction HW mechanics HW electronics Budget Software Management
Changing the conveyer belt
2 screws for wheels
11 screws for the plate
The sticky belt (already attached on the chain) is slided on the rollers

## Slide 15: Adjustments
15
Introduction HW mechanics HW electronics Budget Software Management
Tension in the sticky belt
Moving the axles of the rollers
Held with screws

## Slide 16: Adjustments
16
Introduction HW mechanics HW electronics Budget Software Management
There are some unknown dimensions in components we haven’t ordered yet
We want to have the freedom of adjusting positionning of the motors
STRATEGY
Oblong holes
MOTOR PLATE
PCB PLATE

## Slide 17: Assembly
17
Introduction HW mechanics HW electronics Budget Software Management
Removing the electronic
2 screws for wheels
4 screws for the PCBs
The PCB has to be electrically disconnected from the parts which remain in the robot

## Slide 18: Mechanical components
18
Introduction HW mechanics HW electronics Budget Software Management
Raspberry camera
3D printing
3D printing
360° mirror

## Slide 19: Mechanical components
19
Introduction HW mechanics HW electronics Budget Software Management
list of mechanical components
what we make / buy and where
production process
backup

## Slide 20: Backup plan
20
Introduction HW mechanics HW electronics Budget Software Management

## Slide 21: Electronic assembly
21
Introduction HW mechanics HW electronics Budget Software Management
PCB components
DF Motor Driver
Raspberry Pi
Odroid
Arduino and Arduone

## Slide 22: PCB plate
22
Introduction HW mechanics HW electronics Budget Software Management

## Slide 23: Electrical design
23
Introduction HW mechanics HW electronics Budget Software Management

## Slide 24: Power budget
24
Introduction HW mechanics HW electronics Budget Software Management
 | Part | Vcc [V] | Current [A] | Total consumption [W]
4 | Motors (Wheels) | 6 | 2.4 | 57.6
1 | Motor Conveyor | 6 | 2.4 | 14.4
1 | Raspberry Pi | 5 | 2.5 | 12.5
1 | Raspberry Camera | 5 | 0.25 | 1.25
1 | Odroid | 5 | 4 | 20
1 | USB camera | 5 | 0.15 | 0.75
1 | Arduino | 12 | 0.1 | 1.2
1 | Arduone | 12 | 0.1 | 0.6
10 | Sensors | 5 | 0.05 | 2.5
Margin 50% |  |  |  | 55.4
Total |  |  |  | 162.2
Runtime 20min at 6V |  |  | 9200mAh | 

## Slide 25: Electrical components
25
Introduction HW mechanics HW electronics Budget Software Management
Obtained | On shopping list | Distributor | Arrival
Arduino + Arduone | Odroid (eMMC) | MakerShop | 28th of April
Raspberry Pi | USB Camera | MakerShop | 28th of April
Raspberry Camera | 2x Bumpers | RS Components | 28th of April
IMU | 2x DC converters | RS Components | 28th of April
IR sensors | H-bridge motor driver | EPFL | 6th of May
3x Battery | Cables and Connectors | EPFL / Conrad | 26th of April
5x Motor w/ encoders | Resistors, Capacitances and Regulators | RS Components | 28th of April
Dual H-bridge |  |  | 

## Slide 26: Budget management
26
Introduction HW mechanics HW electronics Budget Software Management
 | Allocated |  | Used | 
 | Internal | External | Internal | External
Mechanical | 1000 | 400 |  | 
Electrical | 700 | 450 | 550 | 0
Reserved | 300 | 150 |  | 
Total | 2000 | 1000 |  | 
Leftover |  |  |  | 
Chart: Budget Usage
| Internal - elec | Internal - meca | External - elec | External - meca
Used | 550 | 0 | 0 | 50
Reserved | 250 | 500 | 450 | 200
Leftover | 200 | 500 | 50 | 250
Used: 600.-
Reserved 1400.-
Leftover: 1000.-

## Slide 27: Budget management
27
Introduction HW mechanics HW electronics Budget Software Management
 | Allocated |  | Used | 
 | Internal | External | Internal | External
Mechanical | 1000 | 400 |  | 
Electrical | 700 | 450 | 550 | 0
Reserved | 300 | 150 |  | 
Total | 2000 | 1000 |  | 
Leftover |  |  |  | 
Chart: Budget Usage
| Internal - elec | Internal - meca | External - elec | External - meca
Used | 550 | 0 | 0 | 50
Reserved | 250 | 500 | 450 | 200
Leftover | 200 | 500 | 50 | 250
Used: 600.-
Reserved 1400.-
Leftover: 1000.-
Chart: 
| Internal used | Internal allocated | Internal planned | External used | External allocated | External planned
Electrical | 550 | 350 | 1000 | 0 | 450 | 500
Mechanical | 0 | 600 | 1000 | 50 | 400 | 500

## Slide 28: Communication schematics
28
Introduction HW mechanics HW electronics Budget Software Management
general architecture of the program
Claudio will do!
Odroid
USB
Cam
RPI
2
RPI
Cam
Ardu-ino
Motor Driver 1
Motor Driver 2
M1
M1
M1
M1
M1
IMU
IR
4x
Encoder
Bumpers
30 fps
30 fps
Bx, By,
Distance
Low frequency
Commands
Pmw, high f
High frequency signals
Command to move to point (x,y), low frequency
Bool: stock
Communication:
ROS Jade

## Slide 29: Software architecture
29
Introduction HW mechanics HW electronics Budget Software Management
general architecture of the program
Claudio will do!

## Slide 30: Bottle detection
30
Introduction HW mechanics HW electronics Budget Software Management
Results

## Slide 31: Obstacle avoidance
31
Introduction HW mechanics HW electronics Budget Software Management
Results

## Slide 32: Localization
32
Introduction HW mechanics HW electronics Budget Software Management
stratégie de ou on va d'abord, etc
pseudo-code
Backup plan!

## Slide 33: Time management
33
Introduction HW mechanics HW electronics Budget Software Management

## Slide 34: Tasks management
34
Introduction HW mechanics HW electronics Budget Software Management
Corrections of the mechanical design
Production of mechanical parts
Ordering of mechanical parts
Prototype of the electrical design
PCB production
Ordering of electrical parts
Computer Vision
Coding
Report Writing
ACHIEVED TASKS
FUTURE TASKS
CURRENT DISTRIBUTION
Mechanical Design
Electronical Design
Software architecture
Building the robot
Tests
Optimisation

## Slide 35
Thank you for your attention
Notes: Questions?